Submission Requirements - Cast Iron Weights

All cast iron weights submitted to the Pennsylvania Standards Laboratory for calibration must be properly prepared before submission according to the following requirements:

- Cast iron weights must be cleaned of all foreign matter such as dirt, rust, grease, concrete, asphalt, and other adhering substances. The laboratory will not calibrate cast iron weights that are contaminated.

- Weights should be sanded or wire brushed to remove any flaking paint or other surface abnormalities.

- If painting is desired, weights should be painted with aluminum paint and allowed to dry for several days.  (Enamel and epoxy paints are not permitted.)

- All weights must have legible serial numbers.

Note: All cast iron weights 10 pounds/5 kilograms and smaller do not meet the specifications for NIST class F.  These weights shall be treated as ASTM class 6.